## Slide 1: High-Performance and Low-Cost Array Signal Processing: Challenges and Trends in Emerging Radar Applications
Rajan Narasimha and Sandeep Rao
Texas Instruments, Inc.
April 7, 2025

## Slide 2: Emerging ADAS Applications: Requirements
Radar with LiDAR like resolution for high-res imaging
  Point clouds and object detection with neural networks (e.g PointNet)
  Velodyne HDL-64E LiDAR ~0.5º resolution @ 20Hz
ADAS example use case
  Pedestrian automatic emergency braking [6] requires angle resolution of ≤ 0.5º deg
Image source: www.ti.com/sensors/mmwave-radar/
https://www.continental-automotive.com/en/components/radars/long-range-radars/advanced-radar-sensor-ars540.html
Key Challenges for High-Res Radar for ADAS
  0.5º deg resolution azimuth and elevation
  Restricted aperture and form factor: ~13cmx9cm
  Dynamic scene => Single snapshot processing, ~50ms frame
  Dynamic range requirements: 20 dB, imposes restrictions on side lobe levels
  Multiple sources in urban environments
13.7cm
9cm
Continental ARS540
Notes: Do we keep industrial
ADAS – azimuth only or azimuth and elevation
L shape antenna coming up
In cabin also can be mentioned

## Slide 3: Classic Radar Processing: Limitations
Classical physics
  Uniform linear array (ULA) with l/2 spacing (~0.2cm spacing for ADAS)
  Spatial BW @ 180° FOV  2/ l
  Half wavelength spacing  Nyquist sampling
Classical algorithms
  Digital beamforming
    Aperture determines resolution
    Rayleigh resolution
    200 ULA elements @ for 0.5° resolution
    ~40cm aperture @ 77 GHz
    Excessive number of antennas and aperture
  Sparse arrays coupled with novel algorithms to combat worse sidelobes  a potential approach
Image source: https://www.mwrf.com/
Notes: Large to be impractical
Sparse array

## Slide 4: Sparse Antenna Arrays: Motivation
Sparse array has larger aperture for the same number of antennas (12)  reduced half-power beam width of main lobe for improved angular resolution/separability
Comes at the expense of side-lobes causing angular ambiguity
Need for more sophisticated algorithms to address ambiguity
Dense ULA with
12 elements (ULA-12)
: M antenna measurements (Mx1)
: Steering matrix (MxN)
sparse source signals (Nx1)
: Noise vector (Mx1)
M = number of antennas
N = number of DoAs in the grid
K = number of true sources or DoAs
Underdetermined system with many solutions
 Impose suitable constraints to extract a suitable solution of
Problem Statement
ULA=Uniform Linear Array
l
Sparse Array with
12 elements (SLA-12)
l

## Slide 5: Sparse Recovery Landscape Overview
+
Combination of problem settings, optimization goals, approaches, analytical tractability and complexity  results in a sizeable landscape of arrays and algorithms being investigated in literature
[1,7,9]
[1,4]
[16]
[19]
[8,14]
[13]
[3]
[11]
[20,22]
[2,5,17]
[1]
[1]
[21]

## Slide 6: Array + Algorithm: Examples
Array | Algorithm | Problem Addressed
Nested/Coprime/Min Red Array | Spatial smoothing + MUSIC | Multiple snapshot + more sources than sensors
Random | OMP, BP, SBL, SPICE… | Gridded: Single/multiple snapshot + high res
Random | NN matrix completion | Gridless: Single/multiple snapshot + high res
Random | Atomic Norm Minimization | Gridless: Single snapshot + high res
Strong interplay between array and algorithm -> some examples
Priors
  Sparse Bayesian learning (SBL) -> Gaussian prior
  Cauchy Gaussian -> Cauchy Prior
  Learning priors through AI/ML -> LISTA
Random Array
Hyperparameters
  No hyperparameter tuning -> e.g, SPICE
  Manual hyperparameter selection -> e.g, Basis Pursuit Denoising
  Learn from data -> e.g, SBL
Ongoing and Future work
  Improving performance under wide range of operating conditions at manageable complexity
  Non integer arrays, distributed arrays
  Learning based methods
  Automatic model order selection and parameter optimization
  H/W optimization and cost-efficient implementations
  Design under constraints
Notes: Pictures for the slides
Specify that single snapshot regime and few snapshots regime is grey area
Much of the detailed analysis is for asymptotic region where large number of snapshots are available
Univ as looking at developing the math and guarantees for a specific problem
Practically what is the number of antennas, expectation on side lobes
Maybe combine the array and algorithm slide to one slide
Show that if we do BP how does the spectrum look
Make it more intuitive – motivate array
Different arrays require different algorithms
Side lobe in the field of view example – this one has side lobe at the edge of the fov

## Slide 7: High Perf. Low Cost Array Signal Processing Trends
Reduction in channel count: An Example
Efficient digital implementation: Examples
  H/W Efficient Embedded Implementation: DSP + FFT Acceleration
Array and Algorithm Co-design
  Spatially smoothed (SS) Music Friendly Arrays
  Array Design For Emerging Antenna Technologies
Current and Future Directions
Notes: Admm acceleration example

## Slide 8: BPDN Algorithm: Performance
CS style approach: Minimize L1 norm while ensuring data fidelity
  L1 norm => A convex optimization problem
  Several solution approaches to solve the optimization
    ISTA, FISTA, ADMM, Homotopy etc.
Performance Comparison for 16 over 80 sparse array
  Resolution probability:
    ~5x improvement over Rayleigh resolution of 16-element ULA
    ~2x improvement over Beamforming for the 16/80 sparse array
  Side lobe levels:
    > 20dB reduction in side-lobe levels compared to beamforming

## Slide 9: Cascade Board Data: DoA Separation = 1o
Data from 86 virtual elements of cascade board
  4 cascaded transceivers with 3tx and 4rx each
  Subsampled measurement at 16 locations with aperture 80 to emulate a random 16 over 80 array
  Compared Bartlett BF with SPICE, BPDN
5x reduction in number of elements for an aperture of 80 elements achieved – while satisfying resolution and SLL requirements
Performance comparison
  Both sparse recovery algorithms can resolve the two corner reflectors placed at 1° separation
  Side lobe levels: BPDN (-160dB) < SPICE (-20dB)
  Note: BPDN has a hyper-parameter to be tuned unlike SPICE
  Demonstrates performance vs complexity trade-offs
TI Cascade EVM

## Slide 10: AWR2944 Functional Block Diagram
C66x DSP core
  >50% allocation for higher level tasks such as tracking
  Desirable to leverage h/w accelerator architecture
Radar H/W Accelerator
  Efficient FFT implementations -> Map sparse-recovery algorithms that leverage FFT acceleration capability of TI SoC

## Slide 11: FISTA Complexity and Implementation
Complexity per iteration dominated by matrix-vector multiplication
  N2 + NM + N, N is grid-size and M is number of antennas
  Compute model assumes second form of equation [21]
  Assumption: M = 32, N = 256, 1000 iterations  74M complex MACs per snapshot [21]
Complexity per iteration dominated by matrix-vector multiplication
  N2 MACs maps to N.logN FFT computation
  Mapped to FFT accelerator
  DSP loading decreases from 74M MACs to 8.1M MACs  9x reduction in the above example
Acceleration of convex optimization methods and fast algorithms for DoA estimation  key direction
[25] Yu Leiming et al, “Efficient Convex Optimization on GPUs for Embedded Model Predictive Control”, MERL Tech Report, 2017
Notes: Refer to MERL ADMM acceleration work

## Slide 12: Array and Algorithm Co-Design: Spatial Smoothed MUSIC
MIMO Structure: Array patterns (1D/2D) conform to a convolution of TX and RX array
Antenna technology
  Series-patch Antenna, Launch-on-package (LoP)
  LoP offers 4.7dB SNR gain, insensitivity to PCB materials
  Antenna dimensions and placement requirements
Super-resolution with MUSIC -> lower complexity than many sparse-recovery algorithms
Conventional MUSIC for super-resolution -> requires multiple snapshots
Single-snapshot MUSIC with Spatial Smoothing -> studied for ULA
LoP Antenna [1]
Series Patch Antenna
[1] 3D Waveguide Antenna Radar System: An RF Independent Substrate Solution, Garcia-Tejero et al., EUMW2022 - Automotive Forum
Not all arrays are suited for SS-MUSIC
SS-MUSIC compatible arrays
  Design 2D array to facilitate 1D SS-MUSIC in azimuth dimension subject to antenna placement requirements
  For applications that are azimuth-heavy
Notes: Most of the literature here assumes several snapshots available -> not viable for automotive
Passive
Array design flow

## Slide 13: 16x16 Array Design Example
Above virtual array has max ULA length = 32 in each row
Largest contained URA size: 26x4
TX Array
RX Array
Virtual Array
Facilitates SS-MUSIC over the azimuth-aperture
L-R symmetry enables FB-averaging

## Slide 14: Azimuth Spectra: SS-MUSIC vs BF
SS-MUSIC exhibits much lower side-lobes than Bartlett BF
Results in superior dynamic range performance
  BF has multiple spurious peaks comparable in amplitude to the source at 23º
As the sources get close to each other, SS-MUSIC is able to resolve, while the BF peaks begin to merge
10dB lower source

## Slide 15: References
[1] M. Pesavento, M. Trinh-Hoang and M. Viberg, "Three More Decades in Array Signal Processing Research: An optimization and structure exploitation perspective," in IEEE Signal Processing Magazine, vol. 40, no. 4, pp. 92-106, June 2023
[2] P. Pal and P. P. Vaidyanathan, "Nested Arrays: A Novel Approach to Array Processing with Enhanced Degrees of Freedom," in IEEE Transactions on Signal Processing, vol. 58, no. 8, pp. 4167-4181, Aug. 2010
[3] D. P. Wipf and B. D. Rao, "Sparse Bayesian learning for basis selection," in IEEE Transactions on Signal Processing, vol. 52, no. 8, pp. 2153-2164, Aug. 2004
[4] P. Stoica, P. Babu and J. Li, "SPICE: A Sparse Covariance-Based Estimation Method for Array Processing," in IEEE Transactions on Signal Processing, vol. 59, no. 2, pp. 629-638, Feb. 2011
[5] A. Moffet, "Minimum-redundancy linear arrays," in IEEE Transactions on Antennas and Propagation, vol. 16, no. 2, pp. 172-175, March 1968
[6] R Wu, “Achieving angular high dynamic range with sparse arrays," in European Microwave Week 2024
[7] Chen, Scott Saobing et al. “Atomic Decomposition by Basis Pursuit.” SIAM J. Sci. Comput. 20 (1998): 33-61.
[8] Sun and Petropulu, "A sparse linear array approach to automotive radar with matrix completion," in ICASSP 2020
[9] D. Malioutov, M. Cetin and A. S. Willsky, "A sparse signal reconstruction perspective for source localization with sensor arrays," in IEEE Transactions on Signal Processing, vol. 53, no. 8, pp. 3010-3022, Aug. 2005
[10] Candes et al., "Towards a Mathematical theory of super-resolution," in arXiv:1203.5871
[11] Li, J., Wu, R., Lu, I.-T., and Ren, D., “Bayesian Linear Regression with Cauchy Prior and its Application in Sparse MIMO Radar”, IEEE Transactions on Aerospace Electronic Systems, vol. 59, no. 6, IEEE, pp. 9576–9597, 2023
[12] Candes, Tao and Rhomberg, “Stable signal recovery from incomplete and inaccurate measurements”, arXiv 2005
[13] C. Lu, J. Tang, S. Yan and Z. Lin, "Nonconvex Nonsmooth Low Rank Minimization via Iteratively Reweighted Nuclear Norm," in IEEE Transactions on Image Processing, vol. 25, no. 2, pp. 829-839, Feb. 2016
[14] Y Chen and Y Chie, "Robust spectral compressed sensing via structured matrix completion," IEEE Transactions in Information Theory, Vol 60, No 10, pp 6576-6601, Oct 2014
[15] P. Sarangi, M. C. Hücümenoğlu and P. Pal, "Single-Snapshot Nested Virtual Array Completion: Necessary and Sufficient Conditions," in IEEE Signal Processing Letters, vol. 29, pp. 2113-2117, 2022
[16] Ilan Ziskind and Mati Wax, "Maximum likelihood localization of multiple source by alternating projection," in IEEE Transactions on Acoustics Speech and Signal Processing, vol. 36, No. 10, pp 1553-1560, Oct 1988
[17] Yuri Abramovich et al, "Positive-definite Topelitz Completion in DoA Estimation for Non-uniform Linear Antenna Arrays - Part 1: Fully Augmentable Arrays," in IEEE Transactions on Signal Processing, vol. 46, No. 9, pp 2458-2571, Sep 1998
[18] Wenjing Liao and Albert Fannjiang , "MUSIC for Single-Snapshot Spectral Estimation: Stability and Super-resolution,” arXiv:1404.1484, Sep 2014
[19] G. Tang, B. N. Bhaskar, P. Shah and B. Recht, "Compressive sensing off the grid," 2012 50th Annual Allerton Conference on Communication, Control, and Computing (Allerton), Monticello, IL, USA, 2012, pp. 778-785.
[20] R. Fu, Y. Liu, T. Huang and Y. C. Eldar, "Structured LISTA for Multidimensional Harmonic Retrieval," in IEEE Transactions on Signal Processing, vol. 69, pp. 3459-3472, 2021
[21] J. Youn, S. Ravindran, R. Wu, J. Li and R. van Sloun, "Circular Convolutional Learned ISTA for Automotive Radar DOA Estimation," 2022 19th European Radar Conference (EuRAD), Milan, Italy, 2022, pp. 273-276
[22] V Monga, Y Li and Y Eldar, “Algorithm unrolling: Interpretable efficient deep learning for signal and image processing”, in arXiv:1912.10557
[23] H Van Trees, “Detection, estimation, and modulation theory: Part IV”, John Wiley & Sons, Incorporated, 2002
[24] I. F. Gorodnitsky and B. D. Rao, "Sparse signal reconstruction from limited data using FOCUSS: a re-weighted minimum norm algorithm," in IEEE Transactions on Signal Processing, vol. 45, no. 3, pp. 600-616, March 1997
[25] Yu Leiming et al, “Efficient Convex Optimization on GPUs for Embedded Model Predictive Control”, MERL Tech Report, 2017

## Slide 16: Machine Learning on the Edge for low-cost mmWave Radars
Sandeep Rao, Texas Instruments
ICASSP 2025, Hyderabad

## Slide 17: Introduction and Context
The previous section focused on improving the angle resolution of a mmWave radar:
  Relevant for Automotive Radars (ADAS) => Larger antenna arrays and sufficient compute for complex algorithms
We’ll now look at radars at the other end of the spectrum:
  Small size, low cost radars => small antenna arrays and minimal compute
  Address emerging applications: Building surveillance, Occupancy sensing, Automotive incabin sensing, Elderly care, HMI
Notes: Radar as a technology is fairly old been around since WW2 – but reason for resurgence in interest is -- smaller size, ….
TI has a family of Radar SoC’s where the …..
6843: 10mm x10mm. AoP =??
6432 : 6.5mmx6.5mm

## Slide 18: Introduction and Context
The previous section focused on improving the angle resolution of a mmWave radar:
  Relevant for Automotive Radars (ADAS) => Larger antenna arrays and sufficient compute for complex algorithms
We’ll now look at radars at the other end of the spectrum:
  Small size, low cost radars => small antenna arrays and minimal compute
  Address emerging applications: Building surveillance, Occupancy sensing, Automotive incabin sensing, Elderly care, HMI
Notes: Radar as a technology is fairly old been around since WW2 – but reason for resurgence in interest is -- smaller size, ….
TI has a family of Radar SoC’s where the …..
6843: 10mm x10mm. AoP =??
6432 : 6.5mmx6.5mm

## Slide 19: The need for Classification
Traditional applications leverage radars strengths in target detection and tracking.
Emerging applications require target classification as well:
Segment | Use-case
Building Automation / Surveillance | Motion Classification (detect intruders while ignoring motion from pets, trees etc.)
Elderly care | Fall Detection , Activity Classification
Gesture Recognition | Mobile Devices, Household appliances, Kick-2-Open (Automotive Boot opener), Automotive Dash Board,

## Slide 20: The need for Classification
Traditional applications leverage radars strengths in target detection and tracking.
Emerging applications require target classification as well:
Radar classification can leverage the work done in the context of Vision. However nature of the signal is different
  Vision: high spatial resolution. None or limited range/velocity resolution
  Radar: High range/velocity resolution. Limited spatial resolution
  Hence intuition on feasibility, performance, and compute complexity has to be built ground up
Segment | Use-case
Building Automation / Surveillance | Motion Classification (detect intruders while ignoring motion from pets, trees etc.)
Elderly care | Fall Detection , Activity Classification
Gesture Recognition | Mobile Devices, Household appliances, Kick-2-Open (Automotive Boot opener), Automotive Dash Board,

## Slide 21: A 30sec intro to Radar Processing
t
Radar Sensor
Range
Velocity
Angle
A radar transmits a series of equi-spaced chirps in a unit called a “frame”
FFT based Signal processing
Reflections of the TX signal are received across multiple RX antennas.
TX signal
RX signal
Signal processing resolves targets in Range, Velocity and Angle
f
f
t
A chirp is a signal whose frequency increases linearly with time
Notes: Radar Signal Processing is a vast and interesting field. But in this slide I’ve tried to summarize the 50,000 feet view of RSP, just enough to give you context for the rest of the talk,

## Slide 22: Resolution of a Radar
Radars have good range and velocity resolution but low cost radars have limited spatial resolution

## Slide 23: Machine Learning on the Edge
It can be difficult to interpret radar output especially in the context of classification problems. ML is a good solution
We will discuss 2 representative examples
  Gesture
  Target classification

## Slide 24: Gesture Recognition

## Slide 25: A typical Radar Signal Chain
PHY processing
Detection
Clustering & Tracking
Source : Machine Learning on the Edge with mmWave Radar IWRL6432. TI application note SWRA774
Tracked point cloud
ADC samples

## Slide 26: Modified for Gesture Recognition (1/2)
CNN extracts features from heatmaps
RNN extracts temporal information
PHY processing
Detection
Clustering & Tracking
Heat map generation
CNN
RNN
Doppler
Range
Source : Machine Learning on the Edge with mmWave Radar IWRL6432. TI application note SWRA774
ADC samples

## Slide 27: Modified for Gesture Recognition (2/2)
PHY processing
Detection
Clustering & Tracking
Heat map generation
Handcrafted
Features
ANN
Doppler
Range
Handcrafted features => lower compute
Source : Machine Learning on the Edge with mmWave Radar IWRL6432. TI application note SWRA774
ADC samples
Notes: Mention how angle also comes in – fuzzy but makes sense

## Slide 28: Processing using Handcrafted features (1/2)
Range-Velocity Heat map is computed for every frame t.
6 hand-crafted features are extracted from this heat map
Range
Doppler
Source : Machine Learning on the Edge with mmWave Radar IWRL6432. TI application note SWRA774

## Slide 29: Processing using Handcrafted features (2/2)
Range
Doppler
The features across 15 consecutive frames are concatenated into a 90x1 vector
This 90x1 vector serves as input to the neural net
3 Layer ANN:
Input layer (60)
Hidden layer (150)
Output layer (7)
Source : Machine Learning on the Edge with mmWave Radar IWRL6432. TI application note SWRA774

## Slide 30: Gesture Recognition – real time example

## Slide 31: Target Classification via Motion Signatures

## Slide 32: Micro-Doppler Signatures
Radars natively have good Velocity resolution.
Can be used to capture the unique “velocity signature” of moving targets
Different targets (bike, pedestrian ,pet, drone, bird, car etc.) can have different “signatures”.
Can be used in target classification/ target filtering.
range
velocity
range
velocity

## Slide 33: Doppler vs Time Spectrogram (1/2)
The relevant slice of the Range Velocity heat map (containing the object of interest) is identified
Range
Doppler

## Slide 34: Doppler vs Time Spectrogram (2/2)
Range
Doppler
Multiple slices across time (i.e. across frames) are used to build up a ‘Velocity-Time image’
These images are sent to an appropriate classifier
Doppler
Time (frames)

## Slide 35: A typical Radar Signal Chain
Tracked point cloud
PHY processing
Detection
Clustering & Tracking
Source : Machine Learning on the Edge with mmWave Radar IWRL6432. TI application note SWRA774
ADC samples

## Slide 36: Modified for Target Classification (1/2)
PHY processing
Detection
Clustering & Tracking
Spectrogram generation
CNN
time
Doppler
Source : Machine Learning on the Edge with mmWave Radar IWRL6432. TI application note SWRA774
Tracked point cloud
ADC samples

## Slide 37: Modified for Target Classification (2/2)
PHY processing
Detection
Clustering & Tracking
Spectrogram generation
Feature extraction
time
Doppler
ANN
Source : Machine Learning on the Edge with mmWave Radar IWRL6432. TI application note SWRA774
Tracked point cloud
ADC samples

## Slide 38: Illustrating Spectrogram signatures

## Slide 39: Summary
PHY processing
Detection
Clustering & Tracking
ADC samples
Tracked point cloud

## Slide 40: Summary
PHY processing
Detection
Clustering & Tracking
Heat map generation
CNN
RNN
Handcrafted
Features
ANN
ADC samples
Tracked point cloud

## Slide 41: Summary
PHY processing
Detection
Clustering & Tracking
Heat map generation
CNN
RNN
Handcrafted
Features
ANN
Spectrogramgeneration
CNN
Handcrafted
Features
ANN
ADC samples
Tracked point cloud

## Slide 42: Summary
PHY processing
Detection
Clustering & Tracking
Heat map generation
CNN
RNN
Handcrafted
Features
ANN
Spectrogramgeneration
CNN
Handcrafted
Features
ANN
features
ANN
ADC samples

## Slide 44: Back up

## Slide 45
Basic Radar PHY processing
Use-case Specific Radar Pre-processing
ML based classifier
ADC data
Classifier output
ML for mmWave Radar | How is it done?
RADAR SIGNAL CHAIN
Example Signatures for Gesture Classification
Notes: The figure shows extracted Doppler signatures which intuitively map to the corresponding actions.
Radar’s have good Doppler resolution – so many classification tasks rely heavily on Doppler based signatures.
More complex signatures can help distinguish more subtle gestures.

## Slide 46
Basic Radar PHY processing
Use-case Specific Radar Pre-processing
ML based classifier
ADC data
Classifier output
ML for mmWave Radar | How is it done?
RADAR SIGNAL CHAIN
Example Signatures for Target Classification
Notes: Here the pre-processing creates an image consisting of the time evolution of the Doppler spectrum.
(again note the reliance on Doppler – a key strength of Radar)
Typically, Moving Humans, pets, Cyclists, Fans, Drones etc tend to have unique Doppler signatures